## Slide 1
time
Sign Server start [exeServer.bat]
Init: SSL server[5005](Load CA, cert, key), load sign key. DB_mgr, [RSA de-crypter]
Start SSL server(5005) wait for request.
Init : UI, SSL client[5005](load CA cert, key), SWATT calculator, [RSA encrypter]
Sign Client start [exeSign.bat]
Select server and try to connect
Connect request
Active login area in UI => User type in
Heartbeat response
SSL verify
Check user [DB]
User + random1
Verify server and fetch user password
Random1+random2/HB
Verify client, authorize user +password [DB]
password + random2
Heart Beat feed back
+ random SWATT challenge.
Select firmware file
Sign the firmware (SSL pri_key)[press button]
Verify data, create server Signature and save the firmware signature to DB,
Server signature/HB
Load server signature to sensor.
Insert data to dataBase
Client end
Client log out
Data base
Sensor reader start[exeSensor.bat]
Init: Sensor UI, client(load CA, cert, key), serial port reader, msg manager.
Init: Sensor registration server thread.
Start SSL server (5006) wait for sensor connection
Connected to sensor and fetch registration info(id, type, version, signature)
XAKA sensor
Select sever and try to connect
Connect request
Generate registration message
Heartbeat response
Verify sensor
Registration
Registration request
Active UI, start to read the data from sensor periodically
Heartbeat response
Registration fail
User close reader
Client logout
Logout the client wait for new connection
# Message sample: ‘C'.encode('utf-8')+dict{‘act’: str, [data]}
# Action type:
# CR - Connection request # SR - Signature response
# HB - Heart beat (feedback) # RG - Sensor Gateway registration.
# LI1 - Login request step 1 [Username + random1(client->sever)]
# LR1 - Login response 1 [random1 + random2(client<-server)]
# LI2 - Login request step2 [random2 + password]
# LR2 - Login response 2 [Challenge for SWATT]
# LO - Logout requst.
# CF - Certificate file fetch.
SSL verify
Firmware Signature
Logout client
DB_mgr(pass in)
signature

## Slide 2
firmwareInfo | 
Index | integer PRIMARY KEY
sensorID | integer NOT NULL
Factory_signerID | integer FOREIGN KEY
Challenge | text NOT NULL
Firmware SWATT | Hex text NOT NULL
Sign Time | text NOT NULL
sensorType | text NOT NULL
firmwareVersion | text NOT NULL
signatureClient | text NOT NULL
SignatureServer | Hex text NOT NULL
userInfo | 
User ID | Text PRIMARY KEY
SALT(random Bx4) | Hex text NOT NULL
SALT+PWD SHA256 | Hex text NOT NULL
Message sample:
‘C'.encode('utf-8')+dict{‘act’: str, [data]}
'F'.encode('utf-8') +fileBytes
# Action type:
# CR - Connection request
# HB - Heart beat (feedback)
# LI1 - Login request step 1 [Username + random1(client->sever)]
# LR1 - Login response 1 [random1 + random2(client<-server)]
# LI2 - Login request step2 [random2 + password]
# LR2 - Login response 2 [Challenge for SWATT]
# CF - Certificate file fetch.
# SR - Signature response
Class A
getVal()
SetVal()
Class B
getVal()
Class C
getVal()
SetVal()
Class D
Class A
getVal()
SetVal()
Class B
getVal()
Class C
getVal()
SetVal()
Class D

## Slide 3
Sign Client [exeSign.bat]
sensor_id + signer_id + swatt_str + time_str + sensor_type + sensor version
Sign
Client private Key[SSL]
Client signature
Sensor info
verify
Client certificate [SSL]
Server [exeServer.bat]
sensor_id + signer_id + swatt_str + time_str + sensor_type + sensor version + Client signature
Sign
Server sign private Key
Server signature
Load in sensor
sensor_id + time_str + sensor_type + sensor version + Server signature
Find record from data base
Compare basic information
Verifiy
[From database] sensor_id + signer_id + swatt_str + date_str + sensor_type + sensor version + Client signature
Server sign certificate

## Slide 4
OPTEE trust application [client <-> server ] design(31/05/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
Hard cord key + IV as parameters
Action:
Create a AES256 cipher operator by load the key and IV.
Encrypt the input buffer[dataBytes] by AES256 and copy to output empty buffer[ciphBytes]
Decrypt the input buffer[ciphBytes] by AES256 and copy to output empty buffer[dataBytes]
TEE driver
1
2
3
4
Normal World [Raspbian]
Client Application
Tee-supplicant service
1. Start OPTEE session
2. OPTEE session confirm
3. Start normal TCP client [5007]
Server
4. Fetch random SWATT challenge string request
5. Send the encrypted bytes
6. Call OPTEE Invoke AES decrypt request and get challenge
7. Calculate SW-ATT
Load AES256 key + IV
Create random challenge str and encrypted by AES256
8. Call OPTEE Invoke AES encrypt request and encrypted SW-ATT output
9. Send the encrypted SWATT
Decode the message and verify the SWATT value
File need to protect

## Slide 5
OPTEE trust application [client <-> server ] design(29/05/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
input: pointer(int)
Output: TEE_SUCCESS/TEE_ERROR_XX
Action:
1. Take pointer’s int value ‘a’ to simulation the SW-ATT input str value <challenge>
2. Calculate a + 100000 to simulation the process to calculate the SW-ATT
3. Feed back normal work action 1 and 2 has been finished.
TEE driver
1
2
3
4
Normal World [Raspbian]
Client Application
Tee-supplicant service
1. Start OPTEE session
2. session confirm
3. Start normal TCP client
Server
4. Fetch random SWATT challenge string
5. Created the encrypted bytes
6. Call OPTEE Invoke AES decrypt
7. Fetch OPTEE point value (SWATT val)
8. Send SWATT val to server
Load AES256 key + IV
Create random challenge str and encrypted