## Slide 1
time
Sign Server start [exeServer.bat]
Init: SSL server[5005](Load CA, cert, key), load sign key. DB_mgr, [RSA de-crypter]
Start SSL server(5005) wait for request.
Init : UI, SSL client[5005](load CA cert, key), SWATT calculator, [RSA encrypter]
Sign Client start [exeSign.bat]
Select server and try to connect
Connect request
Active login area in UI => User type in
Heartbeat response
SSL verify
Check user [DB]
User + random1
Verify server and fetch user password
Random1+random2/HB
Verify client, authorize user +password [DB]
password + random2
Heart Beat feed back
+ random SWATT challenge.
Select firmware file
Sign the firmware (SSL pri_key)[press button]
Verify data, create server Signature and save the firmware signature to DB,
Server signature/HB
Load server signature to sensor.
Insert data to dataBase
Client end
Client log out
Data base
Sensor reader start[exeSensor.bat]
Init: Sensor UI, client(load CA, cert, key), serial port reader, msg manager.
Init: Sensor registration server thread.
Start SSL server (5006) wait for sensor connection
Connected to sensor and fetch registration info(id, type, version, signature)
XAKA sensor
Select sever and try to connect
Connect request
Generate registration message
Heartbeat response
Verify sensor
Registration
Registration request
Active UI, start to read the data from sensor periodically
Heartbeat response
Registration fail
User close reader
Client logout
Logout the client wait for new connection
# Message sample: ‘C'.encode('utf-8')+dict{‘act’: str, [data]}
# Action type:
# CR - Connection request # SR - Signature response
# HB - Heart beat (feedback) # RG - Sensor Gateway registration.
# LI1 - Login request step 1 [Username + random1(client->sever)]
# LR1 - Login response 1 [random1 + random2(client<-server)]
# LI2 - Login request step2 [random2 + password]
# LR2 - Login response 2 [Challenge for SWATT]
# LO - Logout requst.
# CF - Certificate file fetch.
SSL verify
Firmware Signature
Logout client
DB_mgr(pass in)
signature

## Slide 2
firmwareInfo | 
Index | integer PRIMARY KEY
sensorID | integer NOT NULL
Factory_signerID | integer FOREIGN KEY
Challenge | text NOT NULL
Firmware SWATT | Hex text NOT NULL
Sign Time | text NOT NULL
sensorType | text NOT NULL
firmwareVersion | text NOT NULL
signatureClient | text NOT NULL
SignatureServer | Hex text NOT NULL
userInfo | 
User ID | Text PRIMARY KEY
SALT(random Bx4) | Hex text NOT NULL
SALT+PWD SHA256 | Hex text NOT NULL
Message sample:
‘C'.encode('utf-8')+dict{‘act’: str, [data]}
'F'.encode('utf-8') +fileBytes
# Action type:
# CR - Connection request
# HB - Heart beat (feedback)
# LI1 - Login request step 1 [Username + random1(client->sever)]
# LR1 - Login response 1 [random1 + random2(client<-server)]
# LI2 - Login request step2 [random2 + password]
# LR2 - Login response 2 [Challenge for SWATT]
# CF - Certificate file fetch.
# SR - Signature response
Class A
getVal()
SetVal()
Class B
getVal()
Class C
getVal()
SetVal()
Class D
Class A
getVal()
SetVal()
Class B
getVal()
Class C
getVal()
SetVal()
Class D

## Slide 3
Sign Client [exeSign.bat]
sensor_id + signer_id + swatt_str + time_str + sensor_type + sensor version
Sign
Client private Key[SSL]
Client signature
Sensor info
verify
Client certificate [SSL]
Server [exeServer.bat]
sensor_id + signer_id + swatt_str + time_str + sensor_type + sensor version + Client signature
Sign
Server sign private Key
Server signature
Load in sensor
sensor_id + time_str + sensor_type + sensor version + Server signature
Find record from data base
Compare basic information
Verifiy
[From database] sensor_id + signer_id + swatt_str + date_str + sensor_type + sensor version + Client signature
Server sign certificate

## Slide 4
OPTEE trust application [client <-> server ] design(31/05/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
Hard cord key + IV as parameters
Action:
Create a AES256 cipher operator by load the key and IV.
Encrypt the input buffer[dataBytes] by AES256 and copy to output empty buffer[ciphBytes]
Decrypt the input buffer[ciphBytes] by AES256 and copy to output empty buffer[dataBytes]
TEE driver
1
2
3
4
Normal World [Raspbian]
Client Application
Tee-supplicant service
1. Start OPTEE session
2. OPTEE session confirm
3. Start normal TCP client [5007]
Server
4. Fetch random SWATT challenge string request
5. Send the encrypted bytes
6. Call OPTEE Invoke AES decrypt request and get challenge
7. Calculate SW-ATT
Load AES256 key + IV
Create random challenge str and encrypted by AES256
8. Call OPTEE Invoke AES encrypt request and encrypted SW-ATT output
9. Send the encrypted SWATT
Decode the message and verify the SWATT value
File need to protect

## Slide 5
OPTEE trust application [client <-> server ] design(29/05/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
input: pointer(int)
Output: TEE_SUCCESS/TEE_ERROR_XX
Action:
1. Take pointer’s int value ‘a’ to simulation the SW-ATT input str value <challenge>
2. Calculate a + 100000 to simulation the process to calculate the SW-ATT
3. Feed back normal work action 1 and 2 has been finished.
TEE driver
1
2
3
4
Normal World [Raspbian]
Client Application
Tee-supplicant service
1. Start OPTEE session
2. session confirm
3. Start normal TCP client
Server
4. Fetch random SWATT challenge string
5. Created the encrypted bytes
6. Call OPTEE Invoke AES decrypt
7. Fetch OPTEE point value (SWATT val)
8. Send SWATT val to server
Load AES256 key + IV
Create random challenge str and encrypted

## Slide 6
Client Application
OPTEE trust application [client <-> server ] design(10/07/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
Pre-stored Value:
AES default Key, AES IV
Challenge String length
SWATT calculation Iteration time [m]
Linear congruential random(BSD rand MAX and seed offset )
File address block range.
Functions:
Accept the trustClient(normal word) connection.
Load default AES-Key, decrypt msg, get session key. => Set AES session key, decrypt msg and get challenge str.
Create first randomSeed and extract challenge string => random file byte’s address + state list.
Do SWATT calculation for input byte, refresh all the TA(trustWorld) inside parameters.
Return to step 3, repeat n times.
Finished all and get the final SWATT int/hex val.
Load AES-session Key, encrypt SWATT value.
Load AES-session -Key, decrypt msg, get server verify result.
TEE driver
1
1, 2, 3, 4, 5, 7
Normal World [Raspbian]
OPTEE driver <=> Tee-supplicant service
1 - Start OPTEE session
Trust Server thread
0 . Init TCP client and load config file
2.2 - Load AES256 key + IV
=> Create random 32B session key => Encrypt session key
2.3 Fetch Pre-saved program
1, 2, 3, 4, 5, 7
2 – Log in to the trust server
Main server start
Load AES256 key + IV
Login request: F;Gateway_ID;Program_V;Key_Version;C_Len, m, n
2.1 confirm log in
2.1.1 Log in reject.
2.4 Calculate the file SWATT
Database
2.3 Forward session key msg to TA(TrustZone)
2
3.1 Load file in memory and fetch bytes based on the Addr
3 x m
Addr
4. Forward new init seed, swat-seed, state[n], file bytes to TA
4 x m
5. Load the encrypted swatt msg
5
5.1 Decrypt the SWATT feed back msg
6. Verify the SWATT value and create the report
6.1. AES Encrypt the SWATT value + verify result
7. Forward encrypted feedback msg
7
7.1 Load verification result
- Verify success => Terminate
- Verify failed => Remove the checked program. ( or return to step 2 )
7.1
NetWork
8. Check the program running status , System library usage and (memory usage ), encrypt message
8. Decrypt the message and save the program running data.
8
Encrypted AES session key
2.3 Session key setup confirm
2.3 Create the random Swatt Challenge string based on the C_len and encrypted the msg.
2.3 Forward challenge string msg to TA
2

## Slide 7
Train station

## Slide 8
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
0. Load config file
1. OPTEE session
TCP Client
Tee-supplicant service
OPTEE driver
2. Accept OPTEE connection
Raspberry PI
Server Computer
3. Accept the TCP connection

## Slide 9
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Server Computer
Random fetch a AES256 key[A] from key list in TA
OPTEE driver <=> Tee-supplicant service
Key ID
Create Login message
Parse message
F;Gateway_ID;Program_V;Key_ID;C_Len, m, n
Fetch AES56Key [A] based on Key ID form DB
Create random session AES56Key[B] and encrypted the key [B] by [A]
Forward message to TA
Decrypt the message by Key [A] and get the session key [B]
Create random SWATT challenge string and encrypt by session key[B]
Forward message to TA
Decrypt the SWATT challenge by Key [B] and store in trust app buffer.

## Slide 10
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Server Computer
Use the SWATT challenge string get the random block/bytes memory address/file position.
OPTEE driver <=> Tee-supplicant service
Bytes address
Fetch related bytes data from the address
Fetch the pre-saved file base on the message in step1
Encrypt the SWATT final result by AES256 session key[B]
Add bytes to SWATT checksum calculation
Calculate the SWATT checksum value base on the same block size, challenge string and iteration time.
Forward message to Trust-Server
Finished iteration ?
Bytes data
No
Yes
Decrypt the message to get the SWATT value from gate way then compare with the server’s SWATT result.

## Slide 11
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Server Computer
OPTEE driver <=> Tee-supplicant service
Record the program execution data in Database
Encrypt the gateway’s SWATT value and authorization result by session key[B].
Forward message to TA.
Decrypt the message by Key[B], compare the SWATT value and get the authorization result.
Get the program execution information and library dependency, send the message to server
Authorizationreuslt ?
Removed the vulnerable file.
fail
success

## Slide 12
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Server Computer
Random fetch a AES256 key from key list in TA
Random fetch a AES256 key from key list in TA

## Slide 13
HMI computer 192.168.10.21
PLC 1
192.168.10.72
1. Plc coil change cmd
2. Plc coil change feed back
3. Plc state read cmd
4. Plc state feed back
HMI computer 192.168.10.21
PLC 1
192.168.10.72
1. Plc coil change cmd
2. Plc coil change feed back
3. Plc state read cmd
4. Plc state feed back
Respbarry PI
192.168.10.234